## Slide 1
Evaluation of Tracking Regimes for, and Security of PLI Systems
A thesis submitted in partial fulfillment of the requirements for the degree of Master of Science in Computer Engineering
by
Shayan Taheri
Utah State University
Logan, Utah
Summer 2015

## Slide 2
Overview
Introduction
Physical Layer Identification System
Tracking System Models
PLI System Security Evaluation
Conclusion
Acknowledgement
Questions
Notes: These are the topics that are covered in this presentation.

## Slide 3
Introduction
Methods in the area of computer and network security:
  Digital Domain
    Flexible and controllable in design
    Problem: Vulnerable in front of recent cyber attacks
    Example: Leakage of identifiers (username and password)
    Solution: Analog signaling behaviors
  Physical Domain
    Designing methods based on the analog representation of data
    Unique variations for identification and monitoring purposes
Notes: 1) The digital methods are not reliable any more.
2) Solution: Using the analog signaling behaviors of the devices or in other words concentrating on the Physical Domain.
3) In fact, there are unique variations in the analog signals of the devices that can be used for identification and monitoring purposes.
4) These unique features are due to hardware and manufacturing inconsistencies.

## Slide 4
Introduction …
Physical Layer Identification (PLI)
  Using the first layer of the OSI model for identification of the devices
PLI Methodology
  Identify and acquire a certain signal (i.e. Fingerprint)
  Extract a set of meaningful features from the signal
  Compare the test feature set with the reference feature set
  Determination of the device identity
Notes: 1) Fingerprint: A repetitive and always present signal.

## Slide 5
Introduction …
Ethernet card record – Example for fingerprint:
m5c1 card – Experiment 4 , Dataset 8

## Slide 6
Introduction …
PLI System
  Any systematic approach for accomplishment of the PLI operation
  Including: Equipment, Algorithm, …
Experimental Setup for Test PC and DAQ PC

## Slide 7
Introduction …
Employing a PLI system, used for wired Ethernet cards:
  Information profiles for identification of the devices
  Using profiles for understanding the device behavior over time
  Using the steady-state portion of the device’s record for identification
m5c1 card – Experiment 4 , Dataset 8
Notes: 1) Steady-State Portion: It has sufficient amount of information.

## Slide 8
Introduction …
Three main components in each information profile:
  Matched Filter
  Matched filter outputs for all of the collected records
  All of the calculated threshold ranges for acceptance of the upcoming data
The PLI system problem:
  Lack of identification of the devices in different conditions
  Significant changes in the features of the device’s signal
  Solution: Tracking these changes
Notes: 1) Matched filter: An optimal detector that is sensitive enough to perceive the small variations in a device’s signal.
2) Adaptive Thresholding Strategy: It is used for calculating and updating the threshold range for the upcoming data.

## Slide 9
Introduction …
An example of the significant change in the device’s signal
m5c3 card – Experiment 3 , Datasets 5 and 6

## Slide 10
Introduction …
Developing a Tracking System (a.k.a. tracking regime)
  Capable of explaining the amount of variations of a device’s signal
  A Transductive Transfer Learning problem
  System performance: Similarity between the predicted and actual data
Security Evaluation of the PLI System
  Exposing the system to different types of attack
  Attack Type: Generating the forged version of a device’s signal using
  an arbitrary waveform generator (AWG)
Notes: 1) Transductive Transfer Learning Problem:
Finding a target prediction function for the target domain with unlabeled data using labeled source domain data.
2) The strategy of security evaluation is exposing the system to different types of attack.

## Slide 11
Physical Layer Identification System
Matched Filter
Adaptive Thresholding Strategy
APRS Metrics
Experimental Approach
Results

## Slide 12
PLI System – Matched Filter
Maximizing the signal-to-noise ratio of an input signal
Transfer function of the filter:
Matched Filter Output: A value that is a measurement of the closeness of the input signal to the reference signal
Notes: 1) In order to apply the filter on an input signal:
Performing convolution on the time-aligned versions of the matched filter and test signal.
2) The sampling time is determined according to the maximum of matched filter output.

## Slide 13
PLI System – Adaptive Thresholding Strategy
Determining the threshold range for acceptance of the future signals
Updating the threshold range periodically
Notes: 2) To accept or reject the newly acquired signals  Calculating the threshold range
1) Updating the threshold range, Why? Due to the stochastic nature of the device’s signal.

## Slide 14
PLI System – APRS Metrics
Metrics for evaluation of the system performance in device identification
The result parameters for calculation of the system performance metrics:
  True Positive (TP): Correctly rejection of a record
  False Positive (FP): Wrongly rejection of a record
  True Negative (TN): Correctly acceptance of a record
  False Negative (FN): Wrongly acceptance of a record

## Slide 15
PLI System – APRS Metrics …
Accuracy (A), Precision (P), Recall (R), and Specificity (S):

## Slide 16
PLI System – Experimental Approach
The desired objectives for behavioral analysis of the devices:
  Experiment 1: Analyzing the device behavior with respect to the small variations of its surrounding temperature
  Experiment 2: Analyzing the device behavior with respect to the large variations of its surrounding temperature
  Experiment 3: Analyzing the similarities and differences between the device’s signal and the supplied voltages to the circuit’s general bus and the mounted IC
  Experiment 4: Analyzing the device behavior with respect to the factual variations of its surrounding temperature
Notes: 1) Experiment 1, 2, and 3: Two desktop PCs are used as the Test PC and DAQ PC.
2) Experiment 4: Two mini PCs are used as the Test PC and DAQ PC. They are placed in two different rooms.

## Slide 17
PLI System – Experimental Approach …
Data collection for five Ethernet cards
Having two test runs for each experiment
Acquiring the related auxiliary data along with the devices records
Collecting 10,000 numbers of records for each device in each test run

## Slide 18
PLI System – Results
Similarity between the matched filter output and the surrounding temperature
m5c7 card – Experiment 2 , Dataset 4
Notes: 1) Dependency can be observed between the MFO signal and temperature signal.  They have very similar trends.

## Slide 19
PLI System – Results …
PLI System – Results …
Similarity between the matched filter output and the IC’s supply voltage
m5c1 card – Experiment 4 , Dataset 8

## Slide 20
PLI System – Results …
In Datasets 3-4: Effect of large temperature variations
Getting a large number of false positives and low specificity values
Notes: 1) In fact, the process of identifying the devices is disrupted at large variations of the temperature.

## Slide 21
Tracking System Models
Data Preparation Concepts
Data Modeling Techniques
Results

## Slide 22
Tracking System Models – Data Preparation Concepts
Moving Average
  A filter for smoothing out short-term fluctuations of a signal
  Filtering process: Averaging the signal data points in equal length subsets
m5c2 card – Experiment 1 , Dataset 1

## Slide 23
Tracking System Models – Data Preparation Concepts
Moving Average
  Eliminated noise from the signal
m5c2 card – Experiment 1 , Dataset 1
Notes: 1) Autocorrelation: It is the cross-correlation of a signal with itself. It is useful to find obscured patterns in the signal.

## Slide 24
Tracking System Models – Data Preparation Concepts …
Charging/Discharging Trend
  MFO signal shows charging/discharging trend in the device behavior
  Simple Modeling: Using the formulations of series RC circuit
  Advanced Modeling: Using Thermal System Modeling
Thermal System Modeling
  Thermal system operation: Storing and/or transferring the heat flux
  Three mechanisms for heat flow: Conduction, Convection, Radiation
  Energy Balance Theory: Entered Heat = Emitted Heat + Stored Heat
  Similar to electrical circuit modeling

## Slide 25
Tracking System Models – Data Preparation Concepts …
Employed Thermal System Model

## Slide 26
Tracking System Models – Data Modeling Techniques
Linear Regression
  To find a linear relationship between a response variable and one or more explanatory variable(s)
  Predicting future response data using the constructed model
  Residuals: Actual Data – Predicted Data
  R-Squared: To show the model accuracy in predicting data
Smoothing Spline
  Using as a low-pass filter for the system’s output signal
Notes: 1) Smoothing Spline: A dual-purpose technique  Using either as a data predictive model or as a smoothing filter.

## Slide 27
Tracking System Models – Data Modeling Techniques …
An example for scatter plot of linear regression:
m5c2 card – Experiment 1 , Dataset 1

## Slide 28
Tracking System Models – Data Modeling Techniques …
Robust Regression
  Common data modeling technique
    Having certain underlying assumptions
    Example: Normal distribution for error data in linear regression
  Dissatisfaction of these assumptions  Insensibility to the outliers
  Robust Regression  Reduce the influence of outliers
  A common method for this purpose: Least Absolute Residuals
    Finding a line or curve that minimizes the absolute difference of the residuals
Notes: The process of constructing a prediction model is influenced by the outliers.
Outlier  The data points in a signal that they do not follow the pattern of the rest.

## Slide 29
Tracking System Models – Results
50 models were tried to find the most efficient data predictive model
Device’s Surrounding Temperature
  The best option for predicting the device behavior
  An intruder into the device’s signal
  Trend of MFO signal ~ Trend of temperature signal
  Larger variations of the temperature signal  Higher R-Squared value
Strengthening the data prediction process, using:
  IC’s supply voltage signal
  Charging/discharging trend data
Notes: 1) The calculated data for modeling the charging/discharging trend.

## Slide 30
Tracking System Models – Results …

## Slide 31
Tracking System Models – Results …
m5c2 card – Experiment 3 , Dataset 6
Notes: 1) Temperature plays the main role in predicting the matched filter output.

## Slide 32
PLI Systems Security Evaluation
Architecture of Attack
AWG Configuration
Results

## Slide 33
PLI System Security Evaluation – Architecture of Attack
Attacking the PLI system by:
  Signal Replay: Generating the forged version of a device’s signal using
  an arbitrary waveform generator (AWG)
The attacking process consists of two phases:
  Phase 1: Delivering the sampled version of the device’s signal to
  the attacker and PLI system
  Phase 2:
    Generation of a forged version of the acquired signal by the attacker
    Sending the forged signal to the PLI system.

## Slide 34
PLI System Security Evaluation – Architecture of Attack …

## Slide 35
PLI System Security Evaluation – AWG Configuration
Three main components in an AWG structure:
  Source Memory: Location of the sampled version of the device’s signal
  Digital-to-Analog Converter: For generation of a stepped analog waveform with certain characteristics
  Low-Pass Filter: For smoothing the generated signal
Evaluating the AWG’s output quality based on the DAC performance
The most important parameters for the DAC performance analysis:
  Settling Time
  Resolution
Total Harmonic Distortion
Signal-to-Noise Ratio
Notes: 1) Focusing only on the DAC performance and considering the other components to be in their ideal states.

## Slide 36
PLI System Security Evaluation – AWG Configuration …
Settling Time
  The required time for the steady-state of a system’s output (approximately)
  Having inverse relationship with the sampling rate
  Considering a very low value for this parameter
Resolution
  The number of discrete values for the range of values of an analog signal
  Discretizer: For matching between the voltage levels of the signals
Notes: 1) Settling Time  The sampling rate should be less than or equal to the inverse of the settling time.
2) Resolution  Produced number of discrete values over the range of values of an analog signal.
3) Due to the differences between the architectures and sampling rates of the samplers  The voltage levels of the generated signal and original signal might not match.
3) Discretizer: Rounding each data point of the test signal to the nearest voltage level of the desired signal.

## Slide 37
PLI System Security Evaluation – Experimental Approach
Forged Record Generation:
  Having 10,000 collected records for each of the 26 tested Ethernet cards
  Selecting 25 records (i.e. 1001-1025) to be forged
Using two different sampling rates:
  2.0 GS/s (the highest possible value)
The discretizer outcome – close to the actual record voltages:
  Maximum Voltage = 1.982 (V)
Aligning the original and forged records before applying the matched filter
1.0 GS/s
Minimum Voltage = -1.968 (V)
Notes: We wanted to make sure that the devices reached to their stable states.
The forged records were generated at two different sampling rates.
The discretizer outcome shows the maximum and minimum voltages of the forged records are close to those of original records.
To make sure that we don’t get very high or very low matched filter outputs  The records were aligned.

## Slide 38
PLI System Security Evaluation – Results
Small difference between the original and forged records  Mean = 0.021 (V)
1023th record of the m5c8 card - Sampling Rate: 1.0 GS/s rate

## Slide 39
PLI System Security Evaluation – Results …
Forged Records  Larger expected value and dispersion of data  Defended !
Sampling Rate Effect  Not deterministic in getting larger or smaller dispersion
m5c8 card
The generated forged records at 1.0 GS/s (left) and 2.0 GS/s (right) rates
Notes: The matched filter outputs for original and forged records at two different sampling rates.
1) The PLI system can defend itself against this attack.

## Slide 40
Conclusion
PLI System and Tracking System Models
  Device’s surrounding temperature
    Its trend is similar to the matched filter output
    Having large variations  Disruption in identification of the devices
    The best option for prediction of the MFO signal
    Role: Intruder into the circuit activities
Notes: 1) The reason of all of these points is believed to be due to the temperature role.

## Slide 41
Conclusion …
PLI System Security Evaluation
  MFO signals of forged records
    Having larger expected value and dispersion of data
  The PLI system isn’t consistently defeatable

## Slide 42
Acknowledgment
My advisor: Dr. Ryan Gerdes
The committee members: Dr. Tam Chantem and Dr. Reyhan Baktur
My family and friends

## Slide 43
Questions